## Slide 1: PL measurement electronics
Summer 2020

## Slide 2
Computer
Spectrometer Motor
PMT
PFI0 in
10
DAQ 6211
PFI4 out
+5 V
PFI3 in
PFI1 in
PFI2 in
PFI5 out
PFI6 out
GND
GND
PFI7 out
PFI3 in
…
GND
DAQ 6212 (Counter)
11
12
13
24
9
7
50 Ω
Spectrometer motor pin description:
#9 Shutter open (neg.true)
#10 Forward (Direction)
#11 Step
#12 Limit Switch Low (pos.true when open)
#13 Limit Switch High (pos.true when open)
#21 Return
#22 Shutter Open Return
#23 Forward/Return
#24 Step/Return
#26 Limit Switch Low/Return
*Wire colour match the experimental set up.
Photon Counts

## Slide 3: Double Spectrometer Female Cable
Pin # Colour of wire Function
1 Red Motor Phase 1
2 Purple Motor Phase 2
3 Black Motor Phase 3
4 Green Motor Phase 4
18 Black Low Limit
19 Orange ?
20 Blue Motor Ret 1
21 Orange Motor Ret 2
22 Yellow Motor Ret 3
23 White Motor Ret 4
29 Blue AC Ground *
31 Yellow Shutter + 24 V *
36 White Ground
37 Green High Limit
* Hooked up to power supply